## Slide 1
RFID & Servo Motor Control system for Automatic Door Lock

## Slide 2
COMPONENTS NEEDED
Arduino UNO
LED
Breadboard
Wires
Battery
USB-A to B
RFID Module (RC522)

## Slide 3
Introduction to the Components
Battery
Breadboard
Arduino UNO R3
RFID Module

## Slide 4
Connect Arduino GND to Breadboard negative rail

## Slide 5
Connect Arduino 5V to Breadboard positive rail

## Slide 6
Place RFID Module anywhere in the Bread Board

## Slide 7
Connect RFID VCC to 5V of Arduino

## Slide 8
Connect RFID GND to GND of Arduino GND

## Slide 9
Connect Lower BreadBoard Negative Rail to Upper Negative Rail of BreadBoard

## Slide 10
Connect Lower BreadBoard Positive Rail to Upper Positive Rail of BreadBoard

## Slide 11
Connect Arduino GND to Negative rail of Breadboard

## Slide 12
Connect Servo GND to Negative rail of Breadboard

## Slide 13
Connect Servo Positive to Positive rail of Breadboard

## Slide 14
Connect Servo Signal Pin to Arduino Pin 3

## Slide 15
Connect RFID SCK pin to Arduino pin 13

## Slide 16
Connect RFID SDA pin to Arduino pin 10

## Slide 17
Connect RFID MOSI pin to Arduino pin 11

## Slide 18
Connect RFID MISQ pin to Arduino pin 12
Do Not Connect IRQ pin to anywhere.

## Slide 19
Connect RFID RST pin to Arduino pin 9

## Slide 20
Actual image of Circuit connection & Serial monitor

## Slide 21
Complete Pin Connections
13
IRQ

## Slide 22
Code for Arduino IDE
#include <SPI.h>
#include <MFRC522.h>
#include <Servo.h>
#define SS_PIN 10
#define RST_PIN 9
#define LED_G 5 //define green LED pin
#define LED_R 4 //define red LED
#define BUZZER 2 //buzzer pin
MFRC522 mfrc522(SS_PIN, RST_PIN); // Create MFRC522 instance.
Servo myServo; //define servo name
void setup()
{
Serial.begin(9600); // Initiate a serial communication
SPI.begin(); // Initiate SPI bus
mfrc522.PCD_Init(); // Initiate MFRC522
myServo.attach(3); //servo pin
myServo.write(0); //servo start position
pinMode(LED_G, OUTPUT);
pinMode(LED_R, OUTPUT);
pinMode(BUZZER, OUTPUT);
noTone(BUZZER);
Serial.println("Put your card to the reader...");
Serial.println();
}
void loop()
{
// Look for new cards
if ( ! mfrc522.PICC_IsNewCardPresent())
{
return;
} // Select one of the cards

## Slide 23
if ( ! mfrc522.PICC_ReadCardSerial())
{
return;
}
//Show UID on serial monitor
Serial.print("UID tag :");
String content= "";
byte letter;
for (byte i = 0; i < mfrc522.uid.size; i++)
{
Serial.print(mfrc522.uid.uidByte[i] < 0x10 ? " 0" : " ");
Serial.print(mfrc522.uid.uidByte[i], HEX);
content.concat(String(mfrc522.uid.uidByte[i] < 0x10 ? " 0" : " "));
content.concat(String(mfrc522.uid.uidByte[i], HEX));
}
Serial.println();
Serial.print("Message : ");
content.toUpperCase();
if (content.substring(1) == "73 A4 A2 2E"||content.substring(1)=="F3 3A 67 97")
{
Serial.println("Access Granted");
Serial.println();
delay(500);
digitalWrite(LED_G, HIGH);
tone(BUZZER, 500);
delay(300);
noTone(BUZZER);
myServo.write(180);
delay(3000);
myServo.write(0);
digitalWrite(LED_G, LOW);
}

## Slide 24
else {
Serial.println(" Access denied");
digitalWrite(LED_R, HIGH);
tone(BUZZER, 300);
delay(1000);
digitalWrite(LED_R, LOW);
noTone(BUZZER);
}
}