## Slide 1: RFID Sensor module

## Slide 2: What is RFID ?
RFID is short for “radio-frequency identification” and points to a technology whereby a reader catches digital information encoded in RFID tags or smart labels via radio waves.
RFID systems use radio waves at several different frequencies to transfer data.

## Slide 4: RFID system components

## Slide 5: RFID tags: Smart labels
… and a chip attached to it
an antenna, printed, etched or stamped ...
… on a substrate
e.g. a plastic foil ...
A paper label with RFID inside

## Slide 6: Antenna fields: Inductive coupling
5
Transceiver Tag Reader
antenna
RFID
Tag
IC or microprocessor
antenna

## Slide 7: HOW RFID WORKS

## Slide 8: RFID applications
6
Manufacturing and Processing
  Inventory and production process monitoring
  Warehouse order fulfillment
Supply Chain Management
  Inventory tracking systems
  Logistics management
Retail
  Inventory control and customer insight
  Auto checkout with reverse logistics
Security
  Access control
  Counterfeiting and Theft control/prevention
Location Tracking
  Traffic movement control and parking management
  Wildlife/Livestock monitoring and tracking

## Slide 9: Some RFID readers
7

## Slide 10: RFID Module pin outputs

## Slide 11: Pin Functions:
2. SCK (Serial Clock)
Purpose: Provides the clock signal to synchronize data transfer between the microcontroller and the RFID module.
How it works:
  The microcontroller generates the clock, and the RFID module uses it to shift data in or out on MOSI or MISO lines.
  The speed of communication is determined by this clock signal.
1. SDA (Slave Select/Chip Select - SS)
Purpose: Acts as a selection line for the RFID module. It tells the RFID module whether it is being addressed or not.
How it works:
  When low, the RFID module is selected and ready to communicate.
  When high, the RFID module is inactive, allowing other devices on the SPI bus to operate.

## Slide 12
3. MOSI (Master Out Slave In)
Purpose: Used to send data from the microcontroller (master) to the RFID module (slave).
How it works:
  For example, the microcontroller sends commands to configure the RFID module or transmit data.
4. MISO (Master In Slave Out)
Purpose: Used to send data from the RFID module (slave) to the microcontroller (master).
How it works:
  For example, the RFID module sends tag information or status back to the microcontroller.
5. IRQ (Interrupt Request)
Purpose: Used to signal the microcontroller that an event has occurred on the RFID module.
When it triggers:
  When a card is detected, or data is ready to be read or written.
  It reduces the need for continuous polling, saving processor time.

## Slide 13
How They Work Together in SPI Communication:
Microcontroller as Master:
  It generates the clock (SCK).
  It sends data to the RFID module using MOSI.
  It reads data from the RFID module using MISO.
RFID as Slave:
  It listens to the commands on MOSI.
  It sends responses or data on MISO.
  It toggles IRQ to inform the microcontroller about events (optional).
SDA manages control:
  Ensures only one device communicates on the SPI bus by selecting/deselecting the RFID module.

## Slide 14: Application of RFID